## Slide 1: Harmony Graphics Hands-On Training

## Slide 2: Agenda
  Designing with Graphics Composer
    Navigating Basic Widgets and Schemes
  Managing Events
  Dynamic Strings
  Animations
  Running the Final Application

## Slide 3: Hardware Set-up

## Slide 4: Hardware Requirement
SAM9X60 Curiosity
WVGA Display Module with Max-Touch®
External JTAG Debugger
USB Cable for power
FTDI cable
(Optional)

## Slide 5: Software Requirements

## Slide 6: Software Required
MPLAB X IDE Version 6.05
https://ww1.microchip.com/downloads/aemDocuments/documents/DEV/ProductDocuments/SoftwareTools/MPLABX-v6.05-windows-installer.exe
XC32 Compiler Suite Version 4.20
https://ww1.microchip.com/downloads/aemDocuments/documents/DEV/ProductDocuments/SoftwareTools/xc32-v4.20-full-install-windows-x64-installer.exe
MPLAB Harmony 3 Framework
Harmony Software | Version | Download Link (Github)
BSP | v3.14.0 | https://github.com/Microchip-MPLAB-Harmony/bsp.git
Core | v3.11.1 | https://github.com/Microchip-MPLAB-Harmony/core.git
CSP | v3.13.1 | https://github.com/Microchip-MPLAB-Harmony/csp.git
Devices | N/A | https://github.com/Microchip-MPLAB-Harmony/devices.git
Dev_Packs | v3.13.1 | https://github.com/Microchip-MPLAB-Harmony/dev_packs.git
GFX | v3.12.0 | https://github.com/Microchip-MPLAB-Harmony/gfx.git

## Slide 7: Before you start the LAB…

## Slide 8: MPLAB® Code Configurator
Components
MCC Plugin version
MCC Core version
Project Graph
Config Options
Configured using MGC
Code Generation

## Slide 9: Microchip Graphics Composer (MGC)
Design Tree View
Screen Designer
Widgets Tool Box
Object Editor
Screen manager
Schemes manager

## Slide 10: EV Charger Application

## Slide 11: The EV Charger Application
Pressing the plus or minus buttons will change the meter label and the battery level
Green wire animation for the cable
Press + to reach 100%
Pressing green power button takes user back to previous screen
Press – to remove the pop up message

## Slide 12: The EV Charger Application
If idle for 10 s screen saving mode is entered
Press user push button to go back to previous screen

## Slide 13: Task 1
Managing Simple widgets and schemes

## Slide 14: Task 1

## Slide 15: Task 1
Create an MCC project from scratch
Using Microchip Graphics Composer create a design
  Using Asset Manager add: Images, Fonts, Strings
  Add Image, Label and Button widgets
  Add/Modify Schemes
What is Scheme?

## Slide 16: Color Schemes
A color scheme is an arrangement of colors used to draw various parts of a widget
Provides variability in look-and-feel
Scheme List
Scheme Editor
Transparent Scheme

## Slide 17: Widget Customization Using Scheme
Customize the colors of a widget
Scheme Helper

## Slide 18: Scheme Management
Customize Scheme using Scheme editor & color picker
Scheme Manager
Scheme Editor
Scheme Color Picker
Alpha value adds transparency

## Slide 19: Task 2
Managing Events & Screen Transitions

## Slide 20: Task 2

## Slide 21: Events Handling
Event Callbacks
Library Functions
Driver or PLIB Functions
Application Functions
Event Callbacks
Widget Event Callbacks
Pressed
Released
Other
Graphics Library
Screen Event
Widget Event
Touch Input
Property Change
Screen Change
What can callbacks do?
Call library functions to update the UI
Call driver or PLIB functions to control hardware
Call app functions to perform business logic
Screen Event Callbacks
On Hide
On Show
On Update

## Slide 22: Events Management
Using the Event Manager
Event Manager
Interface to enable/disable event callbacks for a screen and all the event-capable widgets in it
Screen0

## Slide 23: Events Management
Using the Object Editor
Enable/disable event callbacks for selected Screen or Widget

## Slide 24: Event Callbacks
Event Code Generation
Callback functions for enabled events are declared and called by the library
Event callback functions must be user-defined in application code
Widget Event Callbacks
Need to be defined in application code
Screen Event Callbacks
Need to be defined in application code
Generated Screen Header File

## Slide 25: Screen Events
Event Callbacks
<Screen>_OnShow()
  Called right after the screen and children widgets are created
    TIP: Use to allocate and initialize run-time screen objects (e.g., strings)
    TIP: Use to restore widget states
<Screen>_OnUpdate()
  Called right before the screen and children widgets are updated and redrawn.
  This is periodically called inside the Legato task.
    TIP: Use to manage screen application states
    TIP: Use to set widget properties
<Screen>_OnHide()
  Called right before the screen and children widgets are destroyed/freed*
    TIP: Use to delete and free allocations for run-time screen objects
    TIP: Use to save widget states
*screens marked ‘persistent’ are not destroyed when hidden and all dynamic allocations are preserved in memory.

## Slide 26: Screen Events
Event Callbacks
MainMenu_OnShow()
Construct dynamic string objects
Restore toggle button state
1
2
MainMenu_OnHide()
Destroy dynamic string objects
1
MainMenu_OnUpdate()
Manage screen state machine
Handle application events
Use library APIs to update Widget properties
Legato Cooker

## Slide 27: <Screen>_OnUpdate()
Best Practices
MainMenu_OnUpdate()
Manage application screen states
Set widget properties (i.e., call Legato Widget APIs here)
Legato Library Task
External Tasks
(Application, Peripheral Drivers)
event
1. Define all callback functions for a screen and widgets inside a screen-specific application source file
  Cleaner project since screen-specific code are in one source file
Screens in Composer
Screen-specific application source files
2. Always call Legato Widget APIs in <Screen>_Update().
  Guarantees that the screen and widgets exist
  Eliminates race condition in RTOS-based projects

## Slide 28: Task 3
Dynamic String and RTC

## Slide 29: Task 3

## Slide 30: Dynamic String
Define a Legato String Object (leFixedString) and allocate memory
  Set a font to the string object
Set the desired Label widget with the String object
Reference: https://github.com/mchpgfx/legato.docs/wiki/How-to-Show-Dynamic-Labels
//Legato string object
leFixedString p_timestring;
leFixedString_Constructor(&p_timestring, p_legatoTimeBuff, MAX_TIME_STRING_LEN *2);
p_timestring.fn->setFont(&p_timestring, (leFont*)& NotoMono14);
Screen1_rtc_label->fn->setString(Screen1_rtc_label, (leString*)&p_timestring);

## Slide 31: Task 4
Sprite Animation Using Canvas
& Importance of HW Overlays and Multi-Layers

## Slide 32: Task 4 - Canvas
Cycle through 14 images

## Slide 33: HW Overlays and Multi-Layers
Using the Integrated Display Controller

## Slide 34: Multi-Layer Compositing
Compositing
Sources
Output Frame
Hello World
Hello World
Compositing*
Combining of visual elements from separate sources into single images
To create the illusion that all those elements are parts of the same scene

## Slide 35: Hardware Compositing
Integrated Controller HW Overlays
Graphics Library
Display Controller
The LCD Controller in Microchip MPUs have multiple hardware overlays
Frame Buffers
Output Frame
Dynamic content with minimal load on the CPU, and no GPU needed.
Hello World
Hello World
HW Overlays
The graphics library renders to a frame buffer for each HW overlay
The display controller composites the overlays into a single frame.

## Slide 36: Behind the Scenes
Memory
(DDR or Internal SRAM)
Layer 0 Frame Buffer
Layer 1 Frame Buffer
Layer 2 Frame Buffer
Multi-Layers using HW Overlays
Legato Graphics Library
Scratch buffer
Integrated Display Controller
Layer Composition

## Slide 37: Pro Tip: Use Layers to Overlay Dynamic Content
Best Practices
Use middle layer for non-interactive, dynamic content
Use top layer for interactive UI controls and static overlays
Static background, drawn once
Can use compressed background images
Save space without sacrificing performance
Show dynamic content without redrawing background
User input is instantly captured
Minimize redraw of controls
Less redraw = better performance

## Slide 38: Pro Tip: Use Layers for Transparency Effects
Best Practices
aria_image_viewer
Use base and middle layers for main screen widgets and controls.
Use top layer to overlay a semi-transparent frame (e.g., help info)
Use effects like fade in/out
Show new content without fully obscuring contents below
Per-pixel or per layer alpha blending
Smooth transparency effects without loading the CPU.

## Slide 39: Graphics Canvas
Virtual Display

## Slide 40: What is the Graphics Canvas?
Display Controller
Virtual Display
A ‘Virtual Display’ software layer for
Storing or pre-rendering Frame with the GFX Library
Configuring the Display Controller Layers to display the Frames
Applying effects like Motion, Sliding Panels, Sprite Animation, Cropping, Screen Transitions and Fade In/Out using Display Controller Layers
GFX
Canvas
Display Driver
Legato Library
Application
Frame data
Display Controller
PLIB
Display Driver IOCTL
Interface Functions
Frame Buffer
Canvas
Object 1
Canvas
Object 2
Canvas
Object 3

## Slide 41: Canvas Object
Graphics Canvas
A Canvas Object contains frame information
Buffer address, resolution, color mode
Layer ID, size, position, alpha
Layer effects status and settings
A Canvas Object is assigned a HW Layer in the Display Controller
Application calls Canvas APIs to set Display and Effects settings
GFX
Canvas
Canvas
Object
Display
Controller
HW Layer
Application

## Slide 42: Composer and Canvas Integration
Graphics Canvas
Each composer Layer is mapped and rendered to a Canvas object at the same z-order**
# Canvas Objects > HW overlays
Allows as many layers/canvas as RAM can support!!!
Pro Tip
Use Layer Editor Options to Hide/Show Layers in the Composer Editor Window

## Slide 43: Application Interface
Using the GFX Canvas
gfx_canvas.c/h – Core module, private functions, glue code to library and display controller driver
gfx_canvas_api.c/h – Public module, interface functions
During Initialization *
Assign HW Layers to Canvas Objects
Set Canvas Window Size
Hide (or Show) Frames at Init
Apply Canvas Settings. HW Layer changes are applied in next VBLANK Period
*legato_climate_control, **legato_dashboard
At Run-time **
Set a Canvas property (Show)
Set multiple Canvas properties

## Slide 44: Application Interface
Start a Move Effect *
Adding Effects
Canvas supports Move and Fade effects***
During Initialization *
Application can register callbacks to be notified of the Effects Status for each Canvas Object
Move a Canvas Object with speed up/down/fixed motion, start/end positions, move steps.
Start a Fade Effect **
Fade a Canvas Object (in Layer 1), with start/end Alpha value, step value
Fade another Canvas Object (in Layer 2), with start/end Alpha value, step value
*legato_climate_control, **legato_dashboard, ***HW overlay dependent

## Slide 45: Canvas Applications
Sprite Animation
GFX Canvas can be used to do sprite animation of multiple RAW images in memory
Images must have the same color mode as Canvas Object
A HW layer is assigned to the Canvas Object
The Pixel Buffer for the Canvas Object is updated to the address of the current image to be shown
RAW Images in DDR (RGBA8888)
HW Layer
Angle | Address | Size | Position
0 | 0x80012070 | 83 * 23 | (627,238)
2 | 0x800120a8 | 86 * 24 | (626, 235)
… |  |  | 
N | 0x80012118 | 87 * 33 | (623, 191)
Graphics Canvas
Application Code
**legato_dashboard
Set the pixel buffer for the canvas, based on needle image address and size in DDR
Set Window based on needle image position and size
Apply the Canvas settings

## Slide 46: Task 4 Implementation
800
480
58x48
161
261
14 images
Use Raw Uncompressed Images!
[…]
Canvas for Sprite

## Slide 47: Task 4 Implementation
Assign Canvas Object 0 to HW Layer 0, Setting Position and size
Assign Canvas Object 1 to HW Layer 1, Setting Position and size
Assign Canvas Object 2 to HW Layer 2, Setting Position and size
1
2
Declaring array
Of sprite images
3
Setting the next sprite image in the array to the required pixel location
Showing the updated Canvas
Assign Canvas Object 3 to HW Layer 2 for sprite, Setting Position and size

## Slide 48: Task 5 & 6
More Animation Techniques

## Slide 49: Task 5
Image Sequence Widget

## Slide 50: Task 6
Panel SetWidth API
After 10 s goes back to previous screen
Appears if Screen0 is idle for 10s

## Slide 51: Task 7
The Final Application

## Slide 52: Modifications
Layer 0 – All assets for “Scene 0” and “Scene 2”
SCENE 0
SCENE 2
Logo Animated using setPosition API

## Slide 53: Modifications
Layer 1 – All assets for “Scene1”
  Widgets set invisible

## Slide 54: Modifications
Layer 2 for Sprite Animation of the Charge Cable

## Slide 55: Modifications
Use Canvas to Swap Scenes

## Slide 56
Questions?
Notes: 5.5 hours in (END)

## Slide 57: Important Resources
MGC Suite Wiki:
  https://github.com/mchpgfx/legato.docs/wiki
Previous Harmony Graphics trainings:
  https://microchiptechnology.sharepoint.com/sites/HumanInterface/SitePages/Legato-Graphics-Workshop-Series.aspx
  Contact Kristy Seymour to gain access to sharepoint Link
  Contains Basic and Advance trainings including recordings of the presentations

## Slide 58: Thank You