## Slide 1: Harmony Graphics Hands-On Training
12/1/2022

## Slide 2: Agenda
  Designing with Graphics Composer Suite
    Navigating Basic Widgets and Schemes
  Managing Events
  Dynamic Strings
  Animations

## Slide 3: Application Design

## Slide 4: Hardware Requirement
SAM9X60 Curiosity
WVGA Display Module
JTAG Debugger
FTDI Cable
USB for power

## Slide 5
Code Generation
Config Options
Project Graph
Components
MPLAB® Code Configurator
Configured using MGC
Notes: Configurator – same one as in Harmony training.
But now here you see the graphics components, Displays, Drivers, Processor, Templates.

## Slide 6
Microchip Graphics Composer (MGC)
Widgets Tool Box
Object Editor
Screen Designer
Design Tree View
Screen manager
Schemes manager
Notes: Designer and it’s main parts. Go thru them with basic description, will discuss in detail later.
Summary: Inclusive development environment that lets you design the graphical UI.

## Slide 7: Task 1
Create an MCC project from Scratch
Using MHC create a design
  Using Asset Manager add: Images, Font, String
  Add Image, Label and Button Widgets
  Add/ Modify Schemes

## Slide 8
Color Schemes
A color scheme is an arrangement of colors used to draw various parts of a widget
Provides variability in look-and-feel
Scheme List
Scheme Editor
Transparent Scheme

## Slide 9
Scheme Management
Scheme Manager
Scheme Editor
Scheme Color Picker
Scheme Helper
Alpha value adds transparency

## Slide 10: Task 2
Understanding HW Overlays & Multi-Layers
Handling Events
  Button Press Event
  Screen Transition

## Slide 11: Hardware Compositing
Integrated Controller HW Overlays
Graphics Library
Display Controller
The LCD Controller in Microchip MPUs have multiple hardware overlays
Frame Buffers
Output Frame
Dynamic content with minimal load on the CPU, and no GPU needed.
Hello World
Hello World
HW Overlays
The graphics library renders to a frame buffer for each HW overlay
The display controller composites the overlays into a single frame.

## Slide 12: Pro Tip: Use Layers to Overlay Dynamic Content
Best Practices
Use middle layer for non-interactive, dynamic content
Use top layer for interactive UI controls and static overlays
Static background, drawn once
Can use compressed background images
Save space without sacrificing performance
Show dynamic content without redrawing background
User input is instantly captured
Minimize redraw of controls
Less redraw = better performance

## Slide 13: Events Handling
Event Callbacks
Library Functions
Driver or PLIB Functions
Application Functions
Event Callbacks
Widget Event Callbacks
Pressed
Released
Other
Graphics Library
Screen Event
Widget Event
Touch Input
Property Change
Screen Change
What can callbacks do?
Call library functions to update the UI
Call driver or PLIB functions to control hardware
Call app functions to perform business logic
Screen Event Callbacks
On Hide
On Show
On Update

## Slide 14: Task 3
Handling Dynamic Strings
  Using RTC

## Slide 15: Task 4
Animation using Graphics Canvas

## Slide 16: What is the Graphics Canvas?
Display Controller
Virtual Display
A ‘Virtual Display’ software layer for
Storing or pre-rendering Frame with the GFX Library
Configuring the Display Controller Layers to display the Frames
Applying effects like Motion, Sliding Panels, Sprite Animation, Cropping, Screen Transitions and Fade In/Out using Display Controller Layers
GFX
Canvas
Display Driver
Legato Library
Application
Frame data
Display Controller
PLIB
Display Driver IOCTL
Interface Functions
Frame Buffer
Canvas
Object 1
Canvas
Object 2
Canvas
Object 3

## Slide 17: Canvas Object
Graphics Canvas
A Canvas Object contains frame information
Buffer address, resolution, color mode
Layer ID, size, position, alpha
Layer effects status and settings
A Canvas Object is assigned a HW Layer in the Display Controller
Application calls Canvas APIs to set Display and Effects settings
GFX
Canvas
Canvas
Object
Display
Controller
HW Layer
Application

## Slide 18: Composer and Canvas Integration
Graphics Canvas
Each composer Layer is mapped and rendered to a Canvas object at the same z-order**
# Canvas Objects > HW overlays
Allows as many layers/canvas as RAM can support!!!
Pro Tip
Use Layer Editor Options to Hide/Show Layers in the Composer Editor Window

## Slide 19: Application Interface
Using the GFX Canvas
gfx_canvas.c/h – Core module, private functions, glue code to library and display controller driver
gfx_canvas_api.c/h – Public module, interface functions
During Initialization *
Assign HW Layers to Canvas Objects
Set Canvas Window Size
Hide (or Show) Frames at Init
Apply Canvas Settings. HW Layer changes are applied in next VBLANK Period
*legato_climate_control, **legato_dashboard
At Run-time **
Set a Canvas property (Show)
Set multiple Canvas properties

## Slide 20: Application Interface
Start a Move Effect *
Adding Effects
Canvas supports Move and Fade effects***
During Initialization *
Application can register callbacks to be notified of the Effects Status for each Canvas Object
Move a Canvas Object with speed up/down/fixed motion, start/end positions, move steps.
Start a Fade Effect **
Fade a Canvas Object (in Layer 1), with start/end Alpha value, step value
Fade another Canvas Object (in Layer 2), with start/end Alpha value, step value
*legato_climate_control, **legato_dashboard, ***HW overlay dependent

## Slide 21: Canvas Applications
Sprite Animation
GFX Canvas can be used to do sprite animation of multiple RAW images in memory
Images must have the same color mode as Canvas Object
A HW layer is assigned to the Canvas Object
The Pixel Buffer for the Canvas Object is updated to the address of the current image to be shown
RAW Images in DDR (RGBA8888)
HW Layer
Angle | Address | Size | Position
0 | 0x80012070 | 83 * 23 | (627,238)
2 | 0x800120a8 | 86 * 24 | (626, 235)
… |  |  | 
N | 0x80012118 | 87 * 33 | (623, 191)
Graphics Canvas
Application Code
**legato_dashboard
Set the pixel buffer for the canvas, based on needle image address and size in DDR
Set Window based on needle image position and size
Apply the Canvas settings

## Slide 22: Task 4 - Implementation
800
480
58x48
178
258
14 images
Use Raw Uncompressed Images!
[…]

## Slide 23
Task 4 - Implementation
Assign Canvas Object 0 to HW Layer 0, Setting Position and size
Assign Canvas Object 1 to HW Layer 1, Setting Position and size
Assign Canvas Object 2 to HW Layer 2, Setting Position and size
1
2
Declaring array
Of sprite images
3
Setting the next sprite image in the array to the required pixel location
Showing the updated Canvas

## Slide 24: Task 5-6
Animation using Image Sequence Widget
  Image sequence widget cycles through series of images
Animation using panel widget setWidth API

## Slide 25: Important Resources
MGC Suite Wiki: https://github.com/mchpgfx/legato.docs/wiki
Previous Harmony Graphics trainings: https://microchiptechnology.sharepoint.com/sites/HumanInterface/SitePages/Legato-Graphics-Workshop-Series.aspx
  Contact Kristy Seymour to gain access to sharepoint Link
  Contains Basic and Advance trainings including recordings of the presentations

## Slide 26
Questions?
Notes: 5.5 hours in (END)

## Slide 27: Thank You